## Slide 1: Distributed Main Processor Design
Ethan Cua, Parshant Juneja, Ravinsher Singh

## Slide 2: Problem definition
Preventing download and execution of malicious code on the vehicle
Mitigating the effects of sensor fooling
Prevent physical devices from accessing hardware & stopping system communication
  Detect devices if they are placed
  Identify blocked signals
Minimizing radio noise generated by vehicle to prevent detection

## Slide 3: Metrics
Robustness
  If a vehicle gets affected, other vehicles can continue operating normally
Return to deterministic states (failsafe)
  If a vehicle is being controlled by an unwanted party, control will be returned to the vehicle.
Situational awareness
  Know where other vehicles are, inform them of vehicle status if necessary
Preventing enemy exploitation in case of capture
  Destroy access to data infrastructure in case of vehicle capture

## Slide 4: Our solution
Two computers per vehicle: one master, one slave
Slave computer
Radio communication enabled
Receives sensor data on vehicle
Pings remote receiver whenever a remote instruction is received.
Read-only access to master computer data.
Master computer
Contains route data (checkpoints) & local area map
Monitors slave computer actions (i.e. direction, speed)
Not directly connected to any RF communications devices, only accessible through physical means
Responsible for rebooting slave computer and taking over during downtime

## Slide 5: Details of solution
The master computer will have a copy of the operational map, and will reference movements made by the slave computer to it and a routing solution consisting of checkpoints
  If the slave moves too far off-course or out of the operational zone, the master will stop the slave computer using a hardware interrupt and take over.
  During this process, a clean reboot of slave is conducted.
  A reboot signal is sent to the rest of the vehicles in the operational zone, to indicate the vehicle is operating on fallback procedures.
The slave computer will always send a radio message in response to receiving one
  Allows remote operator to monitor communications to the autonomous vehicle
  If a vehicle sends a ‘message received’ ping without the operator or nearby vehicles sending something, it can notify remote operators or handlers of the start of a communications attack.

## Slide 6: Solution process
Tiffany Rad, discussed the feasibility of taking over remote vehicles
LTC Chris, discussed the necessity of uptime and the need to react promptly to changes (maintaining adaptability)
Frederica Nelson, discussed the possibility of fooling GPS sensor, leading us to use a solution based on preprogrammed maps. Also discussed fooling/jamming other sensors leading to faulty input. Hardware access is also a big threat in our system.
SSG Stan Walker, discussed the existence of preprogrammed maps, radio protocols, and the danger of a vehicle being physically captured
LTC Chris Orlowski, discussed frequency hopping in existing vehicles, and dangers (and tools) of upcoming autonomous vehicles he’s seen

## Slide 7: Solution Evaluation
Robustness
  Each vehicle has independent master-slave computers, one vehicle will not affect the others if it goes down.
  Reduced dependency on GPS by matching internal position to GPS information
Returning to deterministic state (failsafe)
  Master oversees slave computer’s decisions, and takes control if it determines the slave computer is compromised.
  May have false positives, but no false negatives.
  Reboots slave computer with fresh OS & original code.
  Takes temporary control of vehicle with internal instructions
Situational Awareness
  Master sends compromised signal through radio transmitter to other vehicles (transmit only)
  Slave communicates with other slave computers (receive and transmit)
Preventing enemy exploitation in case of capture
  Mechanical system controlled by master computer to press ‘kill switch’ if it cannot progress with mission.

## Slide 8: Team & Backgrounds
Ravisher Singh
Junior at University of Colorado,Denver ,CS major
Discord: sandhu.singh.ravi #0742
Parshant Juneja
Senior at UC Berkeley as an EECS major
juneja2019@berkeley.edu
Ethan Cua
Junior at SDSU, Computer Engineering major
TheVIllageIdiot#3945, ethancua@gmail.com

## Slide 9: Appendix
https://www.crfs.com/blog/how-to-deal-with-gps-jamming-and-spoofing/
https://spectrum.ieee.org/telecom/security/protecting-gps-from-spoofers-is-critical-to-the-future-of-navigation